## Slide 1: Neutron Wall Loading Update
L. El-Guebaly, A. Jaber,
A. Robinson, D. Henderson
Fusion Technology Institute
University of Wisconsin-Madison
http://fti.neep.wisc.edu/UWNeutronicsCenterOfExcellence
Contributor:
X. Wang (UCSD)
ARIES Project Meeting
Bethesda, MD
April 4 - 5, 2011

## Slide 2: ARIES-ACT New FW/Div Configuration
January 2011 Strawman
Key parameters:
  R = 5.5 m
  a = 1.375 m
  SOL = 10 cm
  Elongation = 2.2
  Fusion power = 1907.4 MW
  Ave. NWL = 2.8 MW/m2
  @ 10 cm from plasma surface
Surface areas:
  Plasma = 475 m2
  FW area:
      IB FW = 139 m2
      OB FW = 313 m2
      IB & OB FW= 452 m2
  Upper & lower divertors:
    IB plate = 22.5 x 2 m2
    Dome = 28 x 2 m2
    OB plate = 21 x 2 m2
    Div total = 143 m2
  FW + Div Surface area = 595 m2
  Area of wall @10 cm from plasma = 547 m2
Main features:
  Curved IB FW (allowing 11 cm extra space at top/bottom)
  Per Kessel,
    OB div plate @ R-a/2
    IB div plate @ R-a

## Slide 3: New vs. Old FW/Div Configuration
Plasma
Old
New
Smaller entrance to divertor region.
More conforming FW to:
  Capture neutrons before reaching divertor
  Allow 11 cm more space at IB top/bottom for DCLL He/LiPb manifolds
  Reducc nuclear heating at IB magnet.

## Slide 4: 3-D NWL Model
  Includes:
    Plasma boundary
    IB & OB FW
    IB & OB div plates and dome.
  FW and divertor segmented vertically and radially to improve accuracy.
  10 million particle history.
  Statistical error < 1%.
MCNP 3-D Model

## Slide 5: Neutron Source Sampling
Options:
  Uniform within plasma boundary.
    Unrealistic, but used to check geometry (1/2011 ARIES presentation by El-Guebaly).
  Three-nested source regions with variable intensity peaking at magnetic axis:
    Good approximation.
    Intensities borrowed from ARIES-RS: 63%, 32%, 5%.
  3. Actual distribution:
    Source density distributed on R-Z grid not available yet.
    Results identical to 3-nested source, except for 10% higher peak at IB midplane (refer to 5/2008 NWL presentation by Wilson).
5%
32%
63%
MCNP 2-D Plot
(3-nested Source Regions)

## Slide 6: Three-nested Source Regions Within Plasma
Neutron Source Intensity:
63%, 32%, 5%
(Example: 10,000 particles random sampling)

## Slide 7: IB and OB Results
Machine Ave NWL (Pf x 0.8/area):
  @ 10 cm from plasma surface 2.8
Peak OB NWL @ OB midplane 4.7
Ave OB NWL 3.6
Peak IB NWL @ IB midplane 3 x 1.1* = 3.3
Ave IB NWL 2.3
______________
* Correction factor for actual source distribution (refer to 5/2008 NWL presentation by Wilson).

## Slide 8: Divertor Results
Machine Ave NWL (Pf x 0.8/area):
  @ 10 cm from plasma surface 2.8
Peak Div NWL 2
Ave Div NWL 0.7
Peak Div
NWL

## Slide 9: Summary of NWL Results
Machine Ave NWL (Pf x 0.8/area):
  @ 10 cm from plasma surface 2.8
Peak IB NWL 3.3
Ave IB NWL 2.3
Peak OB NWL 4.7
Ave OB NWL 3.6
Peak div NWL 2
Ave div NWL 0.7
Peak to average NWL = 1.68

## Slide 10: Conclusions
Peak NWLs will be used to redefine radial builds for ARIES-ACT:
  3.3 MW/m2 for IB
  4.7 MW/m2 for OB
  2 MW/m2 for divertor.
For ASC, peak to average NWL = 1.68 (not 1.5).