## Slide 1: Generalization and Blanket Updates to the ASC
Lane Carlson
ARIES-Pathways Project Meeting
Gaithersburg, MD, July 27-28, 2011

## Slide 2: ASC Progress Overview
New!
  April 2011 SiC strawmen issued: ACT-I & ACT-II
  Presented paper at SOFE on ASC and VASST
  Radial build/blanket generalization
  More input files, better transparency
  Plasma SA, NWL corrected
  Revised April 2011 strawmen, posted online, ACT-Ib
  No major system code runs – most effort on DCLL implementation into overall SiC module

## Slide 3: Action Items Progress from April 2011 meeting
Action items from last meeting:
  Choose strawmen points then issue ACT-I, II and detailed engineering analysis for SiC blanket.
    Completed 4/8/11, posted online under Working Docs:
    http://aries.ucsd.edu/ARIES/WDOCS/system.shtml
  Once DCLL module is converted with generic build structure, issue ACT-III, IV. In-progress
  Separate pumping powers for He and PbLi in SiC blanket. In-progress

## Slide 4: ASC collaboration with VASST demonstrated at June 2011 SOFE meeting

## Slide 5: Real-time filtering demonstrated

## Slide 6: Generic radial build in progress
Generic radial build should allow true modularity of blankets.
Actual implementation is difficult because each blanket requires specific instructions/order for overall geometric build.
Future work
Builds
0 1 2 3 4 5 6 7 8 9 10 11 *
IB SOL First Wall Gap Blanket Gap HT Shield Gap Vac. Vessel Gap TF Coil Gap Bucking Cy*
1.000E-01 1.400E-02 0.000E+00 3.360E-01 1.000E-02 2.400E-01 1.000E-02 4.000E-01 2.000E-02 0.000E+00 0.000E+00 0.000E+00 *
OB SOL First Wall Gap Blanket Gap Blanket II HT Shield Gap Vac. Vessel - - - *
1.000E-01 1.400E-02 0.000E+00 2.860E-01 0.000E+00 4.500E-01 1.500E-01 2.000E-02 2.500E-01 0.000E+00 0.000E+00 0.000E+00 *
VB Div Plate Repl HTS Gap HT Shield Gap Vac. Vessel Cryodome - - - - - *
3.350E-02 1.500E-01 0.000E+00 3.000E-01 2.000E-02 4.000E-01 4.000E-01 0.000E+00 0.000E+00 0.000E+00 0.000E+00 0.000E+00 *
*

## Slide 7: Generic radial build in progress
Each component relies on specific and unique build instructions.
The components build upon and reference other components.
Hence, a different blanket affects all components.
DCLL
SiC
VV + HT Shield
VV
(IB + OB)
VV + Skeleton Ring
VV
(4 components)

## Slide 8: Plasma surface area corrected
Initially, plasma surface area was simplified by elliptical equations.
Now, more accurate discretized formulas use shape parameters:
Shape Parameters | DCLL | SiC-ACT-I
Ro = plasma major radius | 6.0 m | 5.5
a = plasma minor radius | 1.5 m | 1.375
κ = plasma elongation | 2.2 | 2.2
δ = plasma triangularity | 0.6 | 0.7
ζi , ζo = plasma squareness on IB, OB side | 0 | 0
Scrape-off layer | 0.1 m | 0.1
Increase in plasma squareness ζo from zero causes plasma to bulge
Red = elliptical formulas
Blue = more accurate formulas

## Slide 9: Disagreement between ASC and CAD corrected
With addition of SOL, CAD adds uniform 10 cm around plasma.
ASC adds 10 cm proportionally according to formulas.
Hence, SA according to CAD were higher, NWL lower.
Without SOL
With SOL
ASC
CAD

## Slide 10: Updated ACT-I to ACT-Ib, 6/8/11
http://aries.ucsd.edu/ARIES/WDOCS/system.shtml
Same strawman point is used.
Maintenance ports’ volumes, costs were zero. Corrected, slight increase in COE.
Corrected plasma surface area and NWL to use more accurate formulas.
Most hard-wired numbers have been removed and placed in specific input files for better transparency.
Continual documentation and formatting improvements.
NWL ave (plasma surface) [MW/m2]: 3.07
NWL max (plasma surface) [MW/m2]: 4.76
NWL ave (incl. SOL) [MW/m2]: 2.88
NWL max (incl. SOL) [MW/m2]: 4.46

## Slide 11: Input file are more easily modified & accessible
The following were removed from within the code and placed in input files:
Removed: | Placed in:
CD efficiencies, unit costs, FW freq., power | PowerFlow.data
Penetration shielding | PowerFlow.data
Neutron power distribution | PowerFlow.data
Plasma squareness factors for SA calculations | PowerFlow.data
Reference year, projected year for inflation factors | Costing.data
Inflation factors – new input file created | InflationFactors.data
Material properties – density, unit cost, cost base | Materials.data
Divertor in use – T-tube, plate, or finger | Setup.data
Blanket in use – SiC or DCLL | Setup.data
Display mode – “system” or “coe” | Setup.data
Show online

## Slide 12: Generalization of code
“ASC” is actually comprised of 2 generally separate codes, SiC and DCLL, ~50% shared, ~50% unique
Want to merge the two together – too much has been modified in SiC to replicate exact changes to DCLL. Need to integrate DCLL.
“IF” statements are used to designate which portions of code to use.
  e.g. “If DCLL, then use DCLL radial build, else use SiC builds”
Input files are more generic and contain more modifiable information rather than being hidden within code.
Setup
***************************
Select Divertor Design *
type "1" to use, *
"0" to turn off *
1) J. Burke T-tube design *
0 *
2) X. Wang plate design *
1 *
3) X. Wang finger design *
0 *
***************************
Select Blanket Design *
type "1" to use, *
"0" to turn off *
1) SiC blanket *
1 *
2) DCLL blanket *
0 *
***************************
Select Output Format *
type "1" to use, *
"0" to turn off *
1) "COE" production mode *
for scanning parameters *
0 *
2) "SYSTEM" detailed mode *
for analysis on single pt*
1 *
***************************

## Slide 13: Comparing ARIES-AT to ACT-I & II
a,b. A full listing of parameters is available at: http://aries.ucsd.edu/ARIES/WDOCS/system.shtml
c. Recirculated power is sum CD, aux, plasma heating, cryogenic, divertor and blanket pumping power
d. ARIES-AT COE in 2009$ x 1.4323 = 68.03 mills/kWh
Major differences are highlighted.

## Slide 14: Summary & Future Work
Modifications continue to enhance the ASC
  More input files, better transparency, ease of use
Once DCLL module is converted with generic build structure, issue ACT-III, IV.

## Slide 15
Fusion Power Core Printout Example |  |  |  |  |  |  |  |  |  |  | 
by Les Waganer, Feb 2011 |  |  |  |  |  |  |  |  |  |  | 
 |  | Some numbers are for example only |  |  |  |  |  |  |  |  | 
Acct # | Description | Material | Thickness | Area | Volume | Volume Fraction | Theoretical Density | Fraction of Theo Den | Mass | Unit cost installed | Cost
 |  |  | m | m2 | m3 |  | kg/m3 |  | kg | $/kg | M$
22.01.01 | First Wall & Blkt, Replb |  |  | 1390.71 | 664.1541 |  |  |  | 2906 |  | $320,050
 | First Wall |  |  | 507.781 | 7.635 |  |  |  | 85 |  | $7,225
 | First wall, IB | ODS FS | 0.014 | 132.633 | 1.875 | .078? | 7800 | 1.00 | 35 | $85 | $2,975
 | First wall, OB | ODS FS | 0.014 | 375.148 | 5.76 | .078? | 7800 | 1.00 | 50 | $85 | $4,250
 | Blanket |  |  | 507.781 | 546.2831 |  |  |  | 1701 |  | $186,500
 | Blanket, IB |  | 0.233458 | 132.633 | 436.0471 |  |  |  | 581 |  | $60,175
 | Structure | ODS FS |  | See above | See above | .15? | 7800 | 1.00 | 555 | $85 | $47,175
 | Insulating sleeve | SiC |  | See above | See above | .03? | 3200 | 1.00 | 26 | $500 | $13,000
 | Blanket, OB |  | 0.285989 | 375.148 | 110.236 |  |  |  | 1120 |  | $126,325
 | Structure | ODS FS |  | See above | See above | .17? | 7800 | 1.00 | 1045 | $85 | $88,825
 | Insulating sleeve | SiC |  | See above | See above | .03? | 3200 | 1.00 | 75 | $500 | $37,500
22.01.02 | Second Bkt, Life of Plant |  |  | 400 | 125 |  |  |  | 1120 |  | $126,325
 | Blanket II, OB |  | 0.285989 | 400 | 125 |  |  |  | 1120 |  | $126,325
 | Structure | ODS FS |  | See above | See above | .17? | 7800 | 1.00 | 1045 | $85 | $88,825
 | Insulating sleeve | SiC |  | See above | See above | .03? | 3200 | 1.00 | 75 | $500 | $37,500