## Slide 1: Substantiating the ASC & Implementing the DCLL Blanket
Lane Carlson
ARIES Pathways Project Meeting
Gaithersburg, MD, Oct 13-14, 2011

## Slide 2: ASC Progress
New!
  Continuing code modifications to improve credibility, transparency and to add DCLL blanket functionality.
  Power flow diagram to visualize power balance.
  Errors in power flow and balance corrected.
  Errors in radial component builds corrected.
  Preliminary DCLL strawmen presented for comments.

## Slide 3: ARIES Design Nomenclature
Name | Blanket | Physics | Strawman Point
ACT-I | SCLL (SiC self-cooled PbLi) | Aggressive | Issued April 2011
ACT-Ib | SCLL | Aggressive | Re-issued June 2011
ACT-II | SCLL | Conservative | Issued April 2011
ACT-III | DCLL (dual-coolant PbLi) | Aggressive | Forthcoming
ACT-IV | DCLL | Conservative | Forthcoming

## Slide 4: Action Items Progress from July 2011 meeting
Action items from last meeting:
  Complete DCLL system code model
  Complete generic radial build coding
  Issue DCLL strawmen ACT III & IV
Status
Completed
Ongoing
Forthcoming - preliminary strawmen presented today

## Slide 5: Power Flow Diagram
Show in OmniGaffle

## Slide 6
1st error: trying to split the fraction of neutrons to the blanket twice in a redundant manner and not clearly designating IB and OB. This caused a lower P_thermal.
  250 MW reclaimed; ensured counting is not redundant
2nd error: not counting the P_rad_edge fraction to the blanket.
  15 MW reclaimed; all power fractions now accounted for
3rd error: unclear in designation between power required to do the task and electrical power required. All losses are the electrical power required minus the required power.
  50 MW reclaimed; terminology described explicitly
Power Balance Errors

## Slide 7: ✓ Power Balance Check ✓
✓
✓

## Slide 8: SiC Component Builds Corrected
ACT-Ib
Updated
VV & HT shield ragged edge meshing
HT shield – VV gap too large
All gaps were verified
IB div missing

## Slide 9: DCLL Component Builds Corrected
DCLL test case - Before
After - Radial build mimics input file
gap
VV/TF coil obstruction
Skeleton ring – VV gap too large
IB HT shield missing
IB div missing
DCLL blanket implementation complete

## Slide 10: Preliminary DCLL Strawmen Proposed
ARIES-ACT-III (DCLL blanket, aggressive physics)
  R ~ 7.5 m, a = 1.875 m, βN ~ 0.046, NWL ave ~ 2.53 MW/m2, elongation = 2.0
ARIES-ACT-IV (DCLL blanket, conservative physics)
  R ~ 8.75 m, a = 2.19 m, βN ~0.028, NWL ave ~2.16 MW/m2, elongation = 2.2
Divertor is helium-cooled
All costing is 2009$

## Slide 11: Systems code scanning parameters used
DCLL blanket | Range | Resolution
R [m] | 6 - 9 | 0.25
BT [T] | 5.5 - 9.0 | 0.25
βN | 0.025 - 0.058 | 0.001
Qcyl (q95) | 3.6 – 6.0 | 0.2
Q gain | 15 - 40 | 2.5
n/nGr | 0.7 – 1.0 | 0.05
Impurity fraction | 0.001 - 0.003 | 0.001
Plasma elongation | 2.0 - 2.2 | 0.2
~1 M+ points

## Slide 12: Filtering the data
DCLL blanket | ACT-III (aggr.) | ACT-IV (cons.)
P_net_elec | 1000 ± 25 MW | 1000 ± 25 MW
Q_Peak_Divertor | < 7.5 MW/m2 | < 9.0 MW/m2
Bt_max [T] | 6 – 18 | 6 – 18
H98 | < 1.8 | < 1.4
n/nGr | < 1 | < 1
Kappa | = 2.2 | = 2.0
βN | ~4.5 – 6.0 | ~ 2.5 – 3.0

## Slide 13
13
* All costing is 2009$ ** H98 is based on total power including radiation
ACT-III DCLL Preliminary Strawmen Points for Discussion
Aggressive physics
Note: | βN | R (m) | BT (T) | n/nGr | H98 ** | fBS | Paux (MW) | COE (mills)* | Db # | Pt #
preferential | 0.046 | 7.5 | 5.5 | 1 | 1.752 | 0.779 | 124.1 | 67.40 | 1 | 156068
Lowest COE | 0.042 | 7 | 6.25 | 1 | 1.758 | 0.773 | 89.83 | 64.98 | 1 | 130793
Lowest R | 0.045 | 7.25 | 5.75 | 1 | 1.797 | 0.795 | 97.4 | 65.90 | 1 | 252676
Lowest Bt | 0.045 | 7.5 | 5.5 | 0.95 | 1.746 | 0.729 | 110.7 | 65.85 | 1 | 96845
Highest Bt | 0.04 | 7.5 | 6.25 | 0.95 | 1.764 | 0.736 | 109.1 | 67.55 | 1 | 77308
Q gain | Qdivoutb (MW/m2) | Qdivinb (MW/m2) | Ip (MA) | q95 | kappa | Precir (MWe) | Pthermal (MWth) | Ave neutron wall flux (MW/m2)
22.5 | 7.41 | 3.04 | 12.96 | 4.6 | 2.2 | 380.84 | 3189.6 | 2.53
30 | 7.45 | 3.07 | 12.65 | 5 | 2.2 | 298.03 | 3050.0 | 2.81
27.5 | 7.07 | 2.92 | 12.55 | 4.8 | 2.2 | 316.39 | 3036.3 | 2.60
25 | 7.20 | 2.94 | 13.55 | 4.4 | 2.2 | 339.43 | 3147.8 | 2.51
25 | 6.83 | 2.79 | 13.55 | 5 | 2.2 | 332.70 | 3100.5 | 2.48

## Slide 14
ACT-IV DCLL Preliminary Strawmen Points for Discussion
Conservative physics
14
* All costing is 2009$ ** H98 is based on total power including radiation
Note: | βN | R (m) | BT (T) | n/nGr | H98 ** | fBS | Paux (MW) | COE (mills)* | Db # | Pt #
preferential | 0.028 | 8.75 | 7.5 | 1 | 1.32 | 0.562 | 201.1 | 79.95 | 2 | 19889
Lowest COE | 0.029 | 8 | 8 | 1 | 1.38 | 0.603 | 170.9 | 75.15 | 2 | 1504
Lowest R | 0.027 | 7.75 | 9 | 1 | 1.39 | 0.582 | 205.3 | 78.78 | 2 | 82853
Lowest Bt | 0.031 | 8.5 | 7 | 1 | 1.32 | 0.553 | 208.5 | 76.41 | 2 | 4427
Highest Bt | 0.027 | 7.75 | 9 | 1 | 1.39 | 0.582 | 205.3 | 78.78 | 2 | 82853
Q gain | Qdivoutb (MW/m2) | Qdivinb (MW/m2) | Ip (MA) | q95 | kappa | Precir (MWe) | Pthermal (MWth) | Ave neutron wall flux (MW/m2)
15 | 7.69 | 2.98 | 14.9 | 5.4 | 2 | 532.41 | 3517.1 | 2.16
17.5 | 8.82 | 3.43 | 14.01 | 5.6 | 2 | 483.30 | 3469.9 | 2.56
15 | 8.88 | 3.44 | 14.74 | 5.8 | 2 | 553.95 | 3603.0 | 2.81
15 | 8.46 | 3.28 | 15.19 | 4.8 | 2 | 555.56 | 3654.9 | 2.37
15 | 8.88 | 3.44 | 14.74 | 5.8 | 2 | 553.95 | 3603.0 | 2.81

## Slide 15: Would like guidance on:
Edge radiation inboard/outboard split.
Power fraction to low-temperature FWBS (inboard/outboard) and divertor. 1%?
DCLL pumping power split between PbLi and helium.
DCLL pumping power split between inboard/outboard.
SiC blanket pumping power split between inboard/outboard.

## Slide 16: Summary & Future Work
Modifications continue to enhance & clarify the ASC.
  Power balance diagram visualization. Output file will indicate if power balance fails.
  Component builds fixed for SiC & DCLL.
  DCLL preliminary strawmen suggested.
Implement anticipated changes to ACT-Ib and re-issue as ACT-Ic.
After consensus, formally issue ACT-III, IV.
All formally-issued strawmen avaialable online:
http://aries.ucsd.edu/ARIES/WDOCS/system.shtml

## Slide 17: ASC Legend 25.xls “Mods”