## Slide 1: Updated Thermal Performance of Finger-Type Divertors
M. Yoda, S. I. Abdel-Khalik, D. L. Sadowski,
B. H. Mills, and J. D. Rader
G. W. Woodruff School of Mechanical Engineering

## Slide 2: Objectives / Motivation
Objectives
Evaluate thermal performance of gas-cooled divertor designs in support of the ARIES team
  Develop generalized charts for estimating maximum heat flux
  and required coolant pumping power
  Demonstrate how dynamically similar experiments with different coolants can be extrapolated to prototypical conditions with helium
Motivation
Provide design guidance and develop correlations that can be used in system codes
Determine how divertor thermal performance will be affected by changes in material and coolant temperature limits

## Slide 3: Approach
Conduct experiments that span non-dimensional parameters at prototypical conditions
  Instrumented test sections that closely match divertor geometry
  Match nondimensional coolant flow rate (Reynolds number Re) and ratio of solid to coolant thermal conductivities ks / k
  Matching ks / k requires limited set of experiments with (room temperature) He
  Measure cooled surface temperatures and pressure drop  Nusselt number Nu, loss coefficient KL as a function of Re and ks / k
Develop power-law correlations for Nu, KL
  Extrapolate to prototypical conditions to determine

## Slide 4: Finger-Type Divertors
Can accommodate heat fluxes exceeding 10 MW/m2
Cover small area: ~5105 modules for O(100 m2) divertor
HEMP
W
W-alloy
[Diegele et al. 2003; Norajitra et al. 2004; Ihli 2005]
15.8
14 mm
HEMJ
Notes: 4

## Slide 5: GT Test Module
5
q
Coolants: air, helium (He), argon (Ar)
  Re range  8103 1.5105, vs. Rep = 7.5104
  He, Ar from gas cylinders: single-pass experiments
Brass test sections without and with pin fins
  ks / k = 900, 5000, 7000 for He, air, Ar, vs. (ks / k)p
   340 for W- 1% La2O3 at 1200 °C, He at 700 °C
  48 fins: 1 mm dia., 1.2 mm pitch, 2 mm long
  Heated by oxy-acetylene torch: q 2.0 MW/m2
  One round jet (2 mm exit dia) impinges on cooled surface
  Measure coolant mass flow rate , temperatures at inlet, exit (Ti, Te); inlet pressure pi, pressure drop p
  Thermocouples measure temperatures 1 mm from cooled surface
10 mm
5.8
1
2
TCs
1
12 mm
Notes: 5

## Slide 6
Conduction vs. Convection
For test section without fins, numerical simulations  fraction of heat removed by coolant at cooled surface (via convection) varies with coolant
  Remainder of heat conducted through divertor walls
Air
Helium
Argon
Re [/104]
Heat removed at cooled surface [%]
Notes: 6

## Slide 7: Heat Transfer: No Fins
For test section without fins, Nu (Re, ks / k) results for air, He and Ar described by a single power-law correlation (R2 > 0.99)
  Experimental data validated by numerical simulations at different ks/k
Experiments: Air, He, Ar
Simulations: ks/k = 340, 900, 7000
Re [/104]
Nu (ks/k)0.124
Notes: 7

## Slide 8: Heat Transfer: Fins
For test section with fins, experimental results with air, He and Ar suggest that Nu essentially independent of ks / k  most of the heat removed by convection
Results described by a single power-law correlation (R2 > 0.99)
Experiments: Air, He, Ar
Re [/104]
Nu
Notes: 8

## Slide 9: Pumping Power
Loss coefficient KL for air, He, Ar (i.e., different ks / k)
  Fins increase KL (and ) by ~18% at ReP
  Curve-fit data to power-law correlations
Re [/104]
Loss Coefficient KL
 No fins
 Fins
Notes: 9

## Slide 10: Max. Heat Flux: No Fins
at pressure boundary vs. Re
  Ratio of to incident thermal power 
  Max. pressure boundary temp. Ts
  Helium inlet temp. Tin = 600°C
  = 17 MW/m2 at prototypical conditions, vs. original value of 22 MW/m2
 = 10%
15%
Max. incident heat flux [MW/m2]
based on 1.13 cm2 area
Re [/104]
20%
1100°C
1200°C
Ts = 1300°C
Notes: 10

## Slide 11: Max. Heat Flux: Fins
at pressure boundary vs. Re
  Helium inlet temp. Tin = 600°C
   21 MW/m2 at prototypical conditions  fins increase by ~23%, at the cost of 18% greater
 = 10%
15%
Max. incident heat flux [MW/m2]
based on 1.13 cm2 area
Re [/104]
20%
1100°C
1200°C
Ts = 1300°C
Notes: 11

## Slide 12: Conclusions
Performed experimental studies of finger type divertor without and with fins using air, helium and argon
Developed power-law correlations for Nu (Re, ks / k) for divertor without fins, and for Nu (Re) for divertor with fins
  Extrapolations to prototypical conditions suggest maximum heat flux is about 17 MW/m2 for max. temperature of 1200 °C at pressure boundary for divertor w/o fins (for 12 mm dia. tiles, or 1.13 cm2 area): accounting for ks / k reduces extrapolated values of
  Max. heat flux about 21 MW/m2 for divertor with fins: 23% improvement
Developed power-law correlations for KL(Re)
  Extrapolations suggest fins increase coolant pumping power by ~18% at prototypical conditions

## Slide 13: Tasks through Dec. 13
Experimental studies of finger-type and HEMJ divertors without fins at prototypical value of ks / k  340
  Single-pass experiments with He with tool steel test sections
  Increase incident heat flux to ~4-5 MW/m2
Numerical simulations of finger-type divertor with different pin-fin arrays
  Optimize diameter to length, diameter to pitch ratios
  Determine if most of heat removed by convection
Develop generalized correlations for Nusselt number and loss coefficients for finger-type and HEMJ divertors for use in system codes
Start numerical simulations of plate-type divertor at various ks / k
Complete initial configuration of helium test loop
  10 g/s at 10 MPa

## Slide 14: Tasks through June 13
Experimental studies of finger-type divertor with optimized pin-fin array at prototypical value of ks / k  340
  Single-pass experiments with He near room temperature on test sections made of tool steel
  Develop new test section design suitable for high-pressure He loop
Numerical simulations of HEMJ with pin-fin arrays
  Experimental studies of plate-type divertor at ks / k  1200
  Experiments with air: mass flow rates of He too small
Develop generalized correlations for Nusselt number and loss coefficients for plate-type, finned finger-type and finned HEMJ divertors for use in system codes