## Slide 1: 3D Finite Element Analysis for Ribbed Structure Vacuum Vessel
By: Hamed Hosseini
Advisor: Prof. Farrokh Najmabadi

## Slide 2: Introduction & Motivation
Vacuum Vessel
Geometry of the vacuum vessel is taken from CAD, considering the very thin vacuum vessel (5 cm) and 10 cm thick at the beginning
Primary stress is performed by ANSYS Workbench to see if the thinner wall can accommodate the normal pressure loads and overpressure loads ( Motivation: How thin it can be based on the stress analysis).
Double wall ribbed structure as a way to increase the strength of structure , reducing stress intensity and cooling the system is designed and analyzed.
1/16 of Sectors (Symmetry )
10 (m)
11 (m)
Material : SST 316, Yield Stress: 140 MPa, and Working Temperature: 550 K
5(cm), 10(cm)
Solid Single Wall
Double Wall Ribbed Structure

## Slide 3: Boundary Condition
Fixed Bottom
Symmetry (Frictionless)

## Slide 4: Loads
Outside Pressure (1 atm)
Inside Pressure ( zero)
Gravity

## Slide 5: Solid Single Wall VV
Very Thin VV (5-cm)
Very Thin VV (5-cm)
There are lots of over stressed areas > 140 MPa
166 MPa
197 MPa
300 MPa

## Slide 6: Solid Single Wall VV
Thick VV (10-cm)
Thick VV (10-cm)
Almost all the areas are less than the yield point < 140 MPa
40 MPa
100 MPa
123 MPa

## Slide 7: Double Wall Ribbed Structure/ Sandwich Panels
In the solid single wall, material should be added to those areas with high stress intensity to get the stress lower than the yield point
Ribbed structure as a way to add material , increases the strength of structure which helps to reduce the stress intensity with a little increase in mass
Ribbed structure is very similar to the sandwich panel technique
Sandwich plate which is composed of three layers with two thin flat panel upper and lower and a core in between is a very efficient way of providing high bending stiffness and high strength at low weight ( Libove, Hubka 1951)
It provides sufficient space for the He coolant to follow between the ribs
Ribs attached to
the Inner Sheet
Ribs attached to the
outer Sheet

## Slide 8: Rib Configuration
Vertical Ribs or Horizontal Ribs?
Total Thickness of the Double Wall Ribbed Structure?
Thickness of Each Wall (Sheets)?
Thickness of Ribs?
Distance Between Ribs?
Total Number of Ribs?

## Slide 9: Port Ribbed Structure Study
Very Thin VV (5-cm)
Fixed BC/5-cm Thick Port
149 MPa
149 MPa
123 MPa
123 MPa
143 MPa
116 MPa
143 MPa
116 MPa
Less than 5% difference between similar points
Fixed BC

## Slide 10: Horizontal/ Vertical Ribbed Structure?
25cm
4cm
4cm
4cm
2cm
Fixed BC
Frictionless BC (Symmetry)

## Slide 11: Over Stressed Spots
Boundary Conditions
Over Stressed Spots on Ribs
Fixed BC
Frictionless BC (Symmetry)
400 MPa

## Slide 12: Vertical Ribbed Structure
Variety of vertical Ribbed Structures has been designed and analyzed
(different Sheet thicknesses, Rib thicknesses, gap between sheets, distance between sheets)

## Slide 13: Sheet (Wall) Thickness?
Inner Sheet Over Stressed
Outer Sheet Safe
Adding 1cm to the Inner Sheet
Removing 1cm from Outer Sheet
74 MPa
Reasonable stress happens for inner sheet thickness above 3cm
Outer sheet has less stress intensity than the Inner Sheet
The high stress regions happen inside the inner sheet
Outer sheet can be designed with thinner thickness than the inner sheet
200 MPa
3cm
3cm
2cm
4cm

## Slide 14: Rib Thickness ?
2cm x 4cm Rib
2cm x 8cm Rib
2cm
4cm
3cm
3cm
2cm
8cm
Reasonable stress intensity happens for Ribs around 4cm thickness and above
Rib Length
200 MPa
194 MPa
Weak Parameter, less than 5%

## Slide 15: Gap/Distance Between Ribs?
Ratio Gap/Distance: 2/13
Ratio Gap/Distance: 4/20
13cm
20cm
2cm
4cm
Reasonable stress happens for the distance between Ribs less than 25cm
Bigger gap combined with larger distance between ribs gives better stress results
4cm gap combined with 20cm distance between ribs gives better stress distribution comparing the 2cm gap with 13cm distance between ribs
Larger distance between ribs : Less number of ribs, more space for coolant, less computational time, faster convergence
130 MPa
110 MPa

## Slide 16: Comparison
Double wall (Vertical Ribbed)
Very Thin Solid Single wall (5-cm)
142 MPa
100 MPa
116 MPa
90 MPa
143 MPa
100 MPa
Ribbed structure as a way to add material , increases the strength of structure which helps to reduce the stress intensity
In the vertical ribbed structure, the stress amount gets 25-30% lower than its counterpart area on the very thin solid single wall VV (5-cm)

## Slide 17: Mixed Ribbed Structure (Transition)
150 Mpa
Mixed ribbed structure: Horizontal ribs on the top and bottom port wings are required to lead the He coolant throughout the port to the inboard
Horizontal rib at the corner: Transition rib gets over stressed spot at contact regions

## Slide 18: No Horizontal Rib at the Corner
140Mpa
Vertical ribs cover the corner
Solid sheet gets the yield point : 140 MPa

## Slide 19: Totally/Partially Solid Corner
Totally solid corner
Partially solid corner
Top over stressed spots at contact points
Top needs to be partially solid Corner
Bottom over stressed spots at contact points
Bottom needs to be totally solid corner
170 MPa
300 MPa

## Slide 20: Safe Outer/Inner Sheets
94Mpa
102Mpa
108Mpa
74Mpa
Bottom totally solid corner
Top partially solid corner

## Slide 21: Stress Distribution
Safe Vertical/Horizontal Ribs
Outer Sheet
64MPa
100MPa
74 MPa

## Slide 22: Final Port Design Parameters (Mixed Ribbed Structure)
Design Parameter | Size
Distance between vertical ribs | 18-19cm
Distance between horizontal ribs | 25cm
Rib thickness | 4cm x 4cm
Gap between inner and outer sheets | 4cm
Outer wall (Sheet) thickness | 2cm
Inner wall (Sheet) thickness | 4cm

## Slide 23: Whole Vacuum Vessel
All with ribbed structure (Inboard, Ports and doors)
All the ribbed configurations are made based on the stress distribution results
Not identical on the top and bottom
(Stress Reasons)
Door Ribbed Structure

## Slide 24: Inboard
24cm
26cm
Ribs with constant cross section : 4cm x 6 cm
Matching between inboard & outboard rib channels
2cm
4cm
4cm

## Slide 25: Solid wall Stress Distribution
113MPa
95MPa
100MPa
All regions are less than 119MPa
90MPa
96MPa
86MPa

## Slide 26: Ribbed Structure Stress Distribution
All the ribs are less than 100MPa

## Slide 27: Summary & Future Work
A preliminary structural analysis of the vacuum vessel was performed and the locations of high stresses were identified on the solid single wall vacuum vessel
Sandwich Panels theory was used to model the double wall ribbed structure
Sandwich panel/ Double wall ribbed structure as a way to add little material on the structure to increase the bending stiffness and eventually decreasing the stress intensity was considered
Double wall ribbed structure provides us with sufficient space for the He coolant
Mixed ribbed structure configuration was analyzed and designed
Double wall ribbed structure was analyzed and designed for the whole vacuum vessel including the inboard
Matching between coolant channels for the inboard and outboard was considered
Waiting for the disruption load data from UW to add it to the current load for further analysis.
Thermo-Mechanical analysis based on the nuclear heating data from UW